## Slide 1
initialize
Start test/Take secondary voltage measurements
Take primary voltage measurements
Failed message
Incline test
Fail
Fail
Pass
Pass
Another sample?
Yes
REV 3 03-20-19 id-0
Motor test
Fail
Fail
Close test app
No
Pass
Pass
Scan first DUT and read controller software
Pass
Fail

## Slide 2: Initialize
Configure instruments outside function loop
Select instrument ports
Select USB Com port
Load controller configuration with scanner (Part #, Part name, controller specifications, tolerances, etc.)
Type user name and department
Write to data report

## Slide 3: Read Controller Software
Make connections to controller
Scan DUT sample serial number and write to data report
Read controller with USB to UART adapter
Compare software version, current limit, and Ircomp readings against spec sheet
Pass/Fail

## Slide 4: Star test/Take Secondary Voltage Measurement
Switch harness first
Run instruments
Measure console voltage (compare to min/max)
Measure console voltage ripple (compare to min/max)
Load the console output (125%)
Measure console voltage sag (max)
Write values to data report
Pass/Fail

## Slide 5: Incline Test
Switch harness first
Run instruments
Incline up with waveform generator channel 1
Measure output voltage up (compare to wall voltage)
Incline down with waveform generator channel 2
Measure output voltage down (compare to wall voltage)
Measure incline sense and voltage (compare to min/max)
Measure tach (compare to min/max)
Write values to data report
Pass/Fail

## Slide 6: Take Primary Voltage Measurement
Run instruments
Measure primary voltage 15v (FET driver)
Measure primary voltage 5v (micro)
Write values to data report
Pass/Fail

## Slide 7: Motor test
Step 1
Set speed pot to min
Drive PWM to 10% and measure HV bus and LED frequency(5hz)
Drive PWM to 85% and measure motor voltage(DG)
Set speed pot to max and measure motor voltage
Set speed pot to mid and measure motor voltage
Drive PWM to 70%
ramp motor load to 10 amps (5A per second) - 2 seconds. Wait for 1 second after load reaches 10 amps then measure motor voltage
ramp motor load to 2 amps (4A per second) - 2 seconds and set PWM to 45%
ramp motor load to 20 amps (6A per second) - 3 seconds and measure LED frequency(1.42hz - 1.66hz)(1hz on legacy)
wait for 20 seconds after load reaches 20 amps
measure LED frequency
wait for 20 seconds
measure LED frequency
Write values to data report
Pass/Fail

## Slide 8: Another Sample?
Scan next serial number to “Start Test”
or press complete to end test

## Slide 9: Failed Message
Write failed message to data report
Go to “Another Sample?”

## Slide 10: Close app
Close app