## Slide 1
initialize
Start test/Take secondary voltage measurements
Failed message
Incline test and primary voltage measurements
Fail
Fail
Pass
Pass
Another sample?
Yes
REV - 01-17-20 BKL
Motor test
Fail
Close test app
No
Pass
Scan first DUT and read controller software
Pass
Fail

## Slide 2: Initialize
Type user name and department
Select USB Com port
Select instrument ports
Load controller configuration with scanner (Part #, Part name, controller specifications, tolerances, etc.)
Write to data report

## Slide 3: Read Controller Software
Make connections to controller
Scan DUT sample serial number and write to data report
Read controller with USB to UART adapter
Compare software version, current limit, and Ircomp readings against spec sheet
Pass/Fail

## Slide 4: Star test/Take Secondary Voltage Measurement
Measure console voltage on console header (compare to min/max)
Measure console voltage ripple on console header (compare to min/max)
Load the console output with internal digital load (100%)
Measure console voltage sag on console header( compare to max)
Measure sensor voltage through sensor header to console header pass through (compare to max)
Write values to data report
Pass/Fail

## Slide 5: Incline Test
Incline up with waveform generator channel 1
Incline down with waveform generator channel 2
Measure output voltage on incline header (compare to wall voltage)
Measure microprocessor voltage on programming header (compare to min/max)
Measure mosfet driver voltage on input of microcontroller regulator in (compare to min/max)
Write values to data report
Pass/Fail

## Slide 6: Motor test
Set speed pot to mid
Drive PWM to 20%
measure HV bus (compare to min/max)
Measure static load current (compare to running current 2A to 3A)
Measure motor voltage (compare to min/max)
Drive PWM to 30%
Set speed pot to min and measure motor voltage (compare to min/max)
Set speed pot to max and measure motor voltage (compare to min/max)
Drive PWM to 80%
wait for controller to enter current limit and capture measurement (compare to max)
Write values to data report
Pass/Fail

## Slide 7: Another Sample?
Yes/No

## Slide 8: Failed Message
Write failed message to data report
Go to “Another Sample?”

## Slide 9: Close app
Close app